## Slide 1: Online Stability Validation Using Sector Analysis
Joseph Porter, Graham Hemingway,
Nicholas Kottenstette, Gabor Karsai,
Janos Sztipanovits
ISIS, Vanderbilt University

## Slide 2: Basic Problem
Transitioning safety-critical control system designs from Simulink (continuous time) to software (discrete time, distributed implementations)
How do we maintain guarantees for safety, stability, performance, etc…?
Ideally, we would like to focus on correct-by-construction techniques for our design domains (i.e. control and real-time systems design).

## Slide 3: Passivity
Passive systems theory builds on the idea that physical passive systems are compositional with respect to stability [10].
u(t) | Input signals
y(t) | Output signals
S(t) | Stored energy
D(t) | Dissipated energy
 | Power balance equation
 | Energy balance equation
 | Dissipation condition
 | Passivity condition
Passive systems exhibit robustness to time delays and quantization errors, preserving stability [3,4,8].
Parallel and feedback interconnections of passive systems are passive.

## Slide 4: Conic Systems and Sector Analysis
Zames’ generic framework for both continuous-time and discrete-time analysis [21]
Analyze nonlinear control designs for gain and stability
System gain is max( |a|, b )
Interior conic systems (or components) have a bounded output/input ratio for all time
Conic systems are a superset of passive systems (a>=0)
Framework is also compositional (next slide)
u(t)
y(t)
b
a

## Slide 5: Conic Systems and Sector Analysis

## Slide 6: Conic Systems and Sector Analysis: Feedback
Quadrotor helicopters – discrete-time controller is not quite passive[9]:
Hold operation introduces small amounts of energy (quantified by sector bound a).
Fast dynamics aggravate the problem.
Sufficient condition for L2 stability

## Slide 7: Sample Application: Quadrotor Helicopter (Simplified)
Simplified Plant
Dynamics
Simplification for analysis.
Architecture
Control Loops

## Slide 8: Quad Integrator Model
Each controller component implements two loops, with a velocity estimator.
Sensor data scaling/data distribution component.
Reference input scaling.

## Slide 9: Online Sector Analysis
Simulink Version
Limitations
Sector condition is only sufficient.
Sector analyzer approximates.
Analysis requires high precision and worst-case inputs.
Analysis must starting at the beginning of time with reasonable initial conditions.
Evaluation is criteria are design-specific – use carefully.
Integration Example

## Slide 10: Model-Based Design: ESMoL
ESMoL Logical Architecture
ESMoL Deployment Specification
Simulink Design
TrueTime
Simulation

## Slide 11: Model-Based Design: ESMoL
ESMoL Logical Architecture
ESMoL Deployment Specification
Mathworks’ xPC Target
Simulink Design

## Slide 12: Validating a Hardware-In-the-Loop Quadrotor Controller

## Slide 13: Validating a Hardware-In-the-Loop Quadrotor Controller

## Slide 14: Evaluation: Quantization Error Sensitivity by Noise Injection
Quantization noise modeled by discrete-time Gaussian disturbance with variance

## Slide 15: Evaluation: Quantization Error Sensitivity
Quantization noise modeled by discrete-time Gaussian disturbance with variance
We simulated the effects for different quantization models (single, fix16, fix14, fix10) using the noise model.

## Slide 16: Evaluation: Network Delay Simulation by Brute Force
Synchronous delay model (with zero delay possible).
Over 400,000 data sets.

## Slide 17: Evaluation: Network Delays
Synchronous delay model (with zero delay possible).
Over 400,000 data sets.
Data gap corresponds to an odd distribution of delays:
DPH > 0 and DHO = 0 and
DOI = 0 and DIP > 0

## Slide 18: Related Work
Similarities to work in online verification [2,19]
Online statistical techniques for timing and safety
  Sammapun et al [14] – RT-MaC uses stochastic models to check timeliness and reliability for confidence intervals
  Zuliani et al[22] – statistical model checking for Simulink models
Other promising techniques
  Anta/Tabuada[1] - self-triggered control determines sampling triggers online from bounds derived from stability criteria
  Skaf and Boyd [15,16] – offline techniques using constraint models to determine maximum quantization while preserving control objectives

## Slide 19: Future Work
Efficiency and accuracy requirements – is a fixed-point implementation possible?
More comparisons between parameterized simulations and hardware deployment (also against TrueTime).
Compare with models that have known delay sensitivity.
More distant future…
Switched/hybrid systems – is this technique too conservative?
Integration into tools
  Automatic generation into test models
  Use as a condition check in statistical verification models [22]

## Slide 20: Questions?

## Slide 21: References
[1] A. Anta and P. Tabuada. To sample or not to sample: Self-triggered control for nonlinear systems. IEEE Trans. on Aut. Control, PP(99):1 –1, 2010.
[2] H. Barringer, A. Goldberg, K. Havelund, and K. Sen. Rule-based runtime verification. In Verification, Model Checking, and Abstract Interpretation, volume LNCS 2937, pages 277–306. Springer Berlin / Heidelberg, 2004.
[3] N. Chopra, P. Berestesky, and M. Spong. Bilateral teleoperation over unreliable communication networks. IEEE Transactions on Control Systems Tech., 16(2):304–313, Mar 2008.
[4] A. Fettweis. Wave digital filters: theory and practice. Proc. of the IEEE, 74(2):270 – 327, 1986.
[8] N. Kottenstette and P. J. Antsaklis. Stable digital control networks for continuous passive plants subject to delays and data dropouts. In CDC ’07: Proc. of the 46th IEEE Conf. on Decision and Control, pages 4433 – 4440, 2007.
[9] N. Kottenstette and J. Porter. Digital passive attitude and altitude control schemes for quadrotor aircraft. In ICCA ’09: 7th IEEE Intl. Conf. on Control and Automation, Christchurch, New Zealand, 2009.
[10] M. D. la Sen. Some conceptual links between dynamic physical systems and operator theory issues concerning energy balances and stability. Informatica, 16(3):395–406, 2005.
[14] U. Sammapun, I. Lee, and O. Sokolsky. RT-MaC: runtime monitoring and checking of quantitative and probabilistic properties. In 11th IEEE Intl. Conf. on Emb. and Real-Time Comp. Systems and App., pages 147 – 153, Aug 2005.

## Slide 22: References
[15] J. Skaf and S. Boyd. Filter design with low complexity coefficients. IEEE Trans. on Signal Proc., 56(7):3162–3169, Jul 2008.
[16] J. Skaf and S. Boyd. Controller Coefficient Truncation Using Lyapunov Performance Certificate. Intl. Journal of Robust and Nonlinear Control, Mar 2010.
[19] W. Visser, K. Havelund, G. Brat, S. Park, and F. Lerda. Model checking programs. Automated Software Engineering Journal, 10(2), April 2003.
[21] G. Zames. On the input-output stability of time-varying nonlinear feedback systems part one: Conditions derived using concepts of loop gain, conicity, and positivity. IEEE Transactions on Automatic Control, 11(2):228–238, Apr 1966.
[22] P. Zuliani, A. Platzer, and E. M. Clarke. Bayesian statistical model checking with application to stateflow/simulink verification. In HSCC 2010: 13th Intl. Conf. on Hybrid Systems: Computation and Control, pages 12–16, Stockholm, Sweden, Apr 2010.