## Slide 1: High Confidence Design for Distributed Embedded Systems AFOSR MURI
Graduate Student
Collaboration Meeting

## Slide 2: MURI Challenges and Goals
Building networked control systems (UAVs)
  Scalability of analysis and design tools
  Techniques to provide robustness to network uncertainty
Proving that you built the right stuff, and built it correctly
  Certification via DO-178B
    Safety requirements and levels
    Traceability from code
    Avoiding re-verification of the whole design

## Slide 3: Decoupling Methods
Decoupling Controller Properties from Platform Uncertainties
Boyd’s approach
Fettweiss wave digital filters. Sensitivity approach.
Passive network control systems.
Decoupling Function from Timing: Time-Triggered Architecture
Time-triggered architecture
  What requirements does it impose on the platform?
  How does it work in a design flow?
Loose Time-triggered architecture? - less platform restrictions
Compositional Scheduling – even less platform restrictions (more conservative)
Decoupling Component Behavior from Interaction
Simulation in Ptolemy
  Actors capture component (block) behavior
  Directors coordinate actors
  A director can be an actor (hierarchy)
Verification
  BIP

## Slide 4: VU Work in Progress
Toolchain
  ESMoL Language
    Schedulability analysis
    PF-Specific Simulation
    PF-Specific Code Generation
  FRODO Virtual Machine
    Hardware-in-the-Loop Simulation
    Expanded Semantics
    Deadlock analysis
Control Design
  Quadrotor control
  Passivity theory
  Quantization effects
  Network uncertainties
Laboratory
  Hardware in the loop simulator
  Remote access

## Slide 5: Toolchain
Plant Simulation
STARMAC
Soekris Linux Platform
Time-Triggered Resimulation
Platform-Specific Code
Time-Triggered
Virtual Machine
ESMoL/GME
PaNeCS/GME
Gumstix/Robostix
Hummingbird
LMI Passivity Analysis
Constraint-Based Scheduling

## Slide 6: Toolchain
Problems Integrating Tools:
  Semantic variations
  Developer variations

## Slide 7: Toolchain
Target
Language(s)
Target
Language(s)
Target
Language(s)
Problems Integrating Tools:
  Semantic variations
  Developer variations
Solution?: MetaAdapter Architecture
  Nothing too novel – compilers use intermediate languages
  Formalizes the way interpreters are written by hand
  Rockwell-Collins formal methods group uses Lustre as an IL
Front-End
Design
Language(s)
“Flat” Intermediate Language
Target
Language(s)

## Slide 8: Toolchain
Target
Language(s)
Target
Language(s)
Target
Language(s)
Problems Integrating Tools:
  Semantic variations
  Developer variations
Solution?: MetaAdapter Architecture
  Nothing too novel – compilers use intermediate languages
  Formalizes the way interpreters are written by hand
  Rockwell-Collins formal methods group uses Lustre as an IL
Front-End
Design
Language(s)
“Flat” Intermediate Language
Target
Language(s)
Translation Details go Here
Traverse and generate
(simple)
Information feeds back to the designer

## Slide 9: Interesting Problems
Quantization
  Composition by passivity
  Modeling & Analysis
  Putting into the workflow
Mixed MoCs in the VM
  Time-triggered + RM + Event-Driven?
    What makes sense in HC designs?
    How do we implement it?
    How do we model it?
  Scheduling
Integration of Tools
  Verification
    What to verify?
    Where does it fit in a workflow?
    Semantic translation
    Details, details…

## Slide 10: Passivity and Quadrotors
Passive Control Tutorial
  What is passivity?
  Why is it useful?
  How are we using it?
  What are the limitations?
Application to Quadrotor Dynamics
  Dynamic models
  Are quadrotors passive?
  Control design for quadrotors
  Proving stability

## Slide 11: What is passivity?
Interface property of a dynamic system
  Constraint on rate of change of energy in a system.
More formally, the system satisfies:

## Slide 12: Why is it useful?
Interface property of a dynamic system
  Constraint on rate of change of energy in a system.
  This implies Lyapunov stability
  (set Pin to 0 to check)
More formally, the system satisfies:
from Kottenstette (Diss)

## Slide 13: Why is it useful?
Interface property of a dynamic system
  Implies Lyapunov stability
  Compositionality reduces the analysis burden
    Feedback connections are passive
    Parallel connections are passive
Rough scalability numbers:
  Take 10 linear SISO components in a system with three states each
Case | SDP Problem Size | SDP Solver Iters | Approx Runtime
Global Stability Problem | 30x30 | 20 | 4.9 seconds
Decoupled Stability Problems | (3x3 each) x10 | 10 x 8 | 10 x 0.1 seconds

## Slide 14: How are we using it?
Passive Architectures
  Model structures
    Preserving passivity
    Helping passivity
  Design blocks
    Simulink blocks for building and analyzing passive designs
Implementation
  Network structures
    Wave variables
    Power junctions
  Quantization effects
    Wave variables
    Work in progress

## Slide 15: How are we using it?
Multiple Plants,
Single Controller
No assumptions about network delays

## Slide 16: How are we using it?
Multiple Plants,
Single Controller
No assumptions about network delays
Plants
Controller

## Slide 17: How are we using it?
Multiple Plants,
Single Controller
No assumptions about network delays
Plants
Controller
Wave Transform
}
Power Junction

## Slide 18: What are the limitations?
Performance
  Passivity addresses robustness with respect to stability
  Performance robustness is still not well-characterized (platform effects are a big factor)
Theory still in development
  What can we do with it, and how?

## Slide 19: Quadrotor Dynamics
Quadrotor
Motor Compensator
Inner Loop Controller
(Attitude)
Outer Loop
Controller
(Trajectory)
Input Filters
Quadrotor Control Architecture

## Slide 20: Quadrotor Dynamics
Quadrotor
Motor Compensator
Inner Loop Controller
(Attitude)
Outer Loop
Controller
(Trajectory)
Input Filters
Quadrotor Control Architecture

## Slide 21: Quadrotor: Simulink Model
Inner Loop
(Attitude Control)
Outer Loop
(Position Control)
Sensors (GPS +
Accelerometer)
Open up the model and look
Dynamics

## Slide 22: Are quadrotors passive?
Not so much…
…but if we can make the interface passive, then we can use passive techniques.