## Slide 1: New Developments in Model-Integrated Development of High-Confidence Software
Joe Porter, Graham Hemingway, Nicholas Kottenstette,
Harmon Nine, Chris vanBuskirk,
Gabor Karsai, and Janos Sztipanovits
Institute for Software Integrated Systems
Vanderbilt University
Nashville, TN 37205

## Slide 2: Big Picture: High-Confidence Embedded Software Design
Software
Architecture
Models
Software Component Code
Software design
Plant Dynamics
Models
Controller Models
Controller design
System
Architecture Models
Resource
Management
Models
System Platform Design
Certifiable implementations
Integrating verification and validation into tools
Exploring compositional techniques
Emphasize correct-by-construction
Passive control design
Verification
Scheduling
Concurrency/Deadlock
Schedulability
Value domain issues
Model-based Design Flows (GME)
Domain-Specificity (ESMoL)
Support certification processes
Layered Design Concerns
Our Goals
Notes: High-confidence designs have to deal with multiple layers of design concerns. Rather than an all-in-one tool approach that admits the full expressive power of all design languages involved in the process, we’re trying to restrict the design space for each aspect to use constructive techniques to reduce verification burdens. Our approach is to build up modeling tools incrementally as we can identify new areas where the correct-by-construction methods can be applied.

## Slide 3: Big Picture: High-Confidence Embedded Software Design
Software
Architecture
Models
Software Component Code
Software design
Plant Dynamics
Models
Controller Models
Controller design
System
Architecture Models
Resource
Management
Models
System Platform Design
Layered Design Concerns
AFOSR HCDDES MURI Team
https://wiki.isis.vanderbilt.edu/
hcddes
Sponsored by the AFOSR MURI
FA9550-06-0312
and by NSF CPS contract
NSF-CCF-0820088
Notes: We’re starting with the big picture. Beyond our goals we also have a bigger project with many contributors. The AFOSR funded two MURI projects in this area. Our collaborators are at UC Berkeley, Carnegie-Mellon University, and Stanford.

## Slide 4: Development Workflows for Modeling Tools
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Simulink
Simulation
Requirements
Software Modeling
Platform Design
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
High-confidence development involves many activities in different domains of expertise.
Notes: Inputs to our tools are Simulink control designs, but we recognize that distributing those functions quickly leads to violation of the semantic execution model in Simulink. Our goal is to use model integrated computing to pull together all of these aspects of the design in a consistent way, and generate code that maintains the properties of the control design. As mentioned by earlier speakers, these technologies do not exist in a vacuum. Tools and development processes must work together, recognizing that often simply understanding the design problems is the rate-limiting factor.

## Slide 5: Workflow: Control Design
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Simulink
Simulation
RequirementsAssessment
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
Matlab
analysis scripts
Tuning
Software Modeling
Platform Design
1
Control designers create Simulink and Stateflow models to capture and simulate the physical behavior as well as the engineering design. Design verification takes the form of scripts to assess controller performance (e.g. stability, settling time, overshoot) and adjust controller gains.

## Slide 6: Workflow: Import Control Design to ESMoL
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Software Modeling
(Arch/Deployment)
Platform Design
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
ESMoL Modeling Language
Simulink
Model Files (.mdl)
Requirements
Importer
2
The ESMoL domain-specific modeling language (DSML) includes a sublanguage which fully represents Simulink and Stateflow model structures. The tools include a fully automated model importer.
Notes: At ISIS our business is Domain-Specific Modeling Languages.

## Slide 7: Workflow: Software and Hardware Design
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Software Modeling
(Arch/Deployment)
Platform Design
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
ESMoL Modeling Language
Simulink
Simulation
Requirements
3
Software and hardware designers manually enter software designs in GME to describe the software architecture of the Simulink design models, network topology, and deployment of the software components to the hardware.
Notes: Note that the syntactic binding from Simulink components to ESMoL components is very lightweight, so importing a revised design is straightforward and requires only a small amount of model rework. That is foreshadowing…

## Slide 8: Workflow: Software Analysis
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Software Modeling
(Arch/Deployment)
Platform Design
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
ESMoL Modeling Language
Simulink
Simulation
Requirements
4
Round-trip analysis is integrated into the tool environment.
Esched
Tool
DFinder
Model interpreters generate scheduling specifications and import results. BIP analysis is under development.
Sched Spec
Release Times
BIP
Spec
Model
Transformations
Notes: BIP analysis is under development to support extending our execution semantics to asynchronous communications in a safe and constructive way.

## Slide 9: Workflow: Generation & Execution
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Software Modeling
(Arch/Deployment)
Platform Design
Platform/HIL
Simulation
Testing
ESMoL Modeling Language
Simulink
Simulation
Requirements
5
Scheduling
Deadlock
Model interpreters synthesize C code for controller functions and for platform-specific task/messaging wrappers.
Control Functions
Task/Msg
Wrappers
FRODO VM
A platform-independent time-triggered virtual machine provides a synchronous distributed execution environment.
SoftwareGenerator
TrueTime (Simulink)
xPC Target (HIL)
TrueTime provides platform-specific simulation, and the xPC target enables hardware-in-the-loop.

## Slide 10: Workflow: Assessment & Refinement (in progress)
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Platform/HIL
Simulation
Testing
Simulink
Simulation
Scheduling
Deadlock
Control Functions
Task/Msg
Wrappers
FRODO VM
TrueTime (Simulink)
xPC Target (HIL)
Software Modeling
Platform Design
Requirements Assessment
6
Matlab analysis scripts
In the TrueTime and HIL execution environments we can measure the effects of platform uncertainty on controller performance.
Tuning
Control designers can use the same tests to assess controller stability and performance, closing the loop on the design flow.
Notes: Here we close the loop on the design process. Some of us get uncomfortable at the thought of iterating the design, but there are two points we should make here: 1. Often design problems are due to partial understanding, which we don’t discover until later in the integration, verification, and testing phases. Sometimes you have to break the design to address those problems. 2. We want to make the whole process as painless and lightweight as possible, so that we can preserve model artifacts that were not affected by our radical re-design, and quickly rebuild things that were broken. For example, what if we realized late in the game that our control architecture was inadequate, and we needed a more sophisticated control framework instead? We may end up seriously breaking the component structure (including interfaces) to accommodate such a change.

## Slide 11: Workflow: Constructive Methods
CONTROL
DESIGN
SOFTWARE
IMPLEMENTATION
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Simulink
Simulation
Requirements
Software Modeling
Platform Design
Scheduling
Deadlock
Platform/HIL
Simulation
Testing
Constructive design assumptions must be maintained throughout the implementation process.
PASSIVE CONTROL
TECHNIQUES
COMPOSITIONAL
ANALYSIS
Constructive methods rely on component behavior conditions and interconnection rules to guarantee correct behavior, reducing verification burdens.
SYNCHRONOUS EXECUTION/
TIME-TRIGGERED
ARCHITECTURE
Notes: What are we talking about when we say “Constructive Methods”? There are lots of variants out there.

## Slide 12: Quadrotor Design Example
Quadrotor
Motor Compensator
Inner Loop Controller
(Attitude)
Outer Loop
Controller
(Inertial Position)
Trajectory
Generator
Quadrotor Control Architecture
CONTROL
DESIGN

## Slide 13: Quadrotor: Simulink
Quadrotor
Inner Loop Controller
(Attitude)
Outer Loop Controller
(Inertial Position) and Trajectory Generator
CONTROL
DESIGN

## Slide 14: Quadrotor Software Design: GME & ESMoL
Processor
SOFTWARE
IMPLEMENTATION
Port == Message Instance
Block == Component Instance
Bus
Node Ports == Comm Channels
Component Assignment
Message
Assignment
Peripherals
Platform Design
Model
Logical Architecture
(Dataflow)
Software
Deployment

## Slide 15: Quadrotor Platform Simulation with TrueTime
TrueTime Simulink Model (mdl)
Task Execution Code (C)
Component Timing Parameters:
TTSchedule – start times
ExecPeriod
WC Duration
SOFTWARE
IMPLEMENTATION
GENERATION
& EXECUTION
Time-Triggered
Nodes
Time-Triggered Network
Resolution 5us
Proc RS 4MHz 0s 0s
Comp InnerLoop =50Hz 1ms
Comp DataHandling =50Hz 1ms
Comp ADC =50Hz 1us
Comp SerialIn =50Hz 1ms
Comp SerialOut =50Hz 1ms
Msg DataHandling.sensor_data 8B RS/ADC RS/DataHandling
Msg DataHandling.pos_ref 8B RS/SerialIn RS/DataHandling
Msg InnerLoop.thrust_commands 8B RS/InnerLoop RS/SerialOut
Msg LocalOrder 1B RS/DataHandling RS/InnerLoop
Proc GS 100MHz 0s 0s
Comp OuterLoop =50Hz 1ms
Bus TT_I2C 100kb 1ms
Msg OuterLoop.ang_ref 8B GS/OuterLoop RS/InnerLoop
Msg DataHandling.pos_msg 8B RS/DataHandling GS/OuterLoop
Schedule Spec
SOFTWARE
ANALYSIS
Generated Task Execution Code
ESMoL Model
File (mga)
Scheduler Spec (.scs)
Hyperperiod 20 ms
GS/OuterLoop_0 9.495
RS/SerialIn_0 7.75
RS/ADC_0 8.995
RS/InnerLoop_0 9.495
RS/DataHandling_0 10.495
RS/SerialOut_0 11.865
TT_I2C/OuterLoop.ang_ref_0 9.175
TT_I2C/DataHandling.pos_msg_0 10.815
Scheduler Result (.rslt)
Importer
Generator
Scheduler
Calculated Schedule

## Slide 16: Quadrotor: TrueTime Execution and Schedule
Primary execution loop is an embedded
Time-Triggered scheduler
Time-triggered execution schedule for one Node
Tracking performance is close to ideal…
…but platform effects are successfully simulated
GENERATION
& EXECUTION

## Slide 17: Work in Progress: Online Sector Search
Sector search works in simulation as well as in software, so we can adjust gains for platform effects and iterate the design evaluation process.
Fast quadrotor dynamics introduce a small amount of active behavior. Sector search relates control gain to an interval behavior bound abstraction.
CONTROL
DESIGN
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
Example: Quadrotor position tracking uses a passive PD controller, and we validate the position gain using sector search around the gain loop ( Kx < -1/a ).
See Kottenstette [1]
for details.

## Slide 18: Work in Progress: Statistical Model Checking
We extended the Simulink Quadrotor model with a random (Poisson-distributed in time and duration ) sensor fault. When the fault occurs, all of the sensor outputs return zero.
Statistical model checking sees the system as a black box, so we used an LTL error condition on the measured trajectory. “For 500 seconds of the trace, it will never be true that the error of either x, y, or z will exceed the specified bound for more than 50 seconds.”
¬ F[500] G[50] ( ex > 400 | ey > 400 | ez > 100 )
How did we do? Well, it shouldn’t crash more than 10% of the time under these fault conditions…
CONTROL
DESIGN
Requirements
Assessment
See Zuliani [5]
for details.

## Slide 19: Work In Progress: Fixed Wing Aircraft Example
Multicore Experiment: Deploying multiple control loops to the Cell processor.
Questions to be answered:
Design coverage
Online stability assessment for backstepping designs
We wanted to try our hand at a more complex control design…
Sensor
Data Handler
Gamma Chi Controller
Velocity
Controller
Omega
Controller
Alpha Beta Mu Controller
Cessna
Plant

## Slide 20: Work in Progress: Test and Tap
We want to compare simulated data traces to those collected from the platform for various test cases and tap points. Our prototype test generator automates data generation, execution, data collection, and comparison. It’s still fairly limited…
CONTROL
DESIGN
SOFTWARE
ANALYSIS
GENERATION
& EXECUTION
One problem with complex systems is assessing operational data values inside the system (tap the data streams). This is a job for… grad students!

## Slide 21: Where would we like to go?
Modeling Concepts
  Requirements modeling and management
Design examples
  Coordinated flight
Synthesis tools
  Automated controller design (IDA-PBC for Port Hamiltonian systems)
  Platform-specific function templates
Modeling Semantics
  Asynchronous execution models
  Characterization of the interactions and conflicts between layered design domains
Analysis
  Reducing response time
  Performance optimization

## Slide 22: Questions?
Those interested in trying our tools can visit
https://wiki.isis.vanderbilt.edu/hcddes/index.php/The_ESMoL_Tool

## Slide 23: References
[1] N. Kottenstette, J. Porter. Digital Passive Attitude and Altitude Control Schemes for Quadrotor Aircraft. IEEE 7th Intl. Conf. on Control and Automation (ICCA 2009). Christchurch, New Zealand, Dec. 2009.
[2] Porter, J., P. Volgyesi, N. Kottenstette, H. Nine, G. Karsai, and J. Sztipanovits, "An Experimental Model-Based Rapid Prototyping Environment for High-Confidence Embedded Software", Rapid System Prototyping (RSP'09), Paris, France, Jun. 2009.
[3] J. Porter, G. Hemingway, C. vanBusKirk, N. Kottenstette, G. Karsai, J. Sztipanovits. Online Dynamic Stability Verification Using Sector Search. ACM Intl. Conf. on Embedded Software (EMSoft) Grenoble, Oct. 2010.
[4] G. Hemingway, J. Porter, N. Kottenstette, H. Nine, C. vanBuskirk, G. Karsai, and J. Sztipanovits. Automated Synthesis of Time-Triggered Architecture-based TrueTime Models for Platform Effects Simulation and Analysis. Rapid Systems Prototyping (RSP), Jun. 2010.
[5] P. Zuliani, A. Platzer, E. M. Clarke. Bayesian Statistical Model Checking with Application to Stateflow/Simulink Verification. HSCC 2010 (Hybrid Systems: Computation and Control), Apr. 12-16, 2010, Stockholm, Sweden.
[6] LeBlanc, H., E. Eyisi, N. Kottenstette, X. Koutsoukos, and J. Sztipanovits, "A Passivity-Based Approach To Deployment In Multi-Agent Networks", Informatics in Control, Automation and Robotics (ICINCO 2010), Funchal, Madeira - Portugal, Jun. 2010.
[7] R. Thibodeaux. The Specification and Implementation of a Model of Computation. M.S. Thesis. Vanderbilt University, May 2008.
[8] N. Kottenstette, "Constructive Non-Linear Control Design With Applications to Quad-Rotor and Fixed-Wing Aircraft", Tech. Rpt., Inst. for Software Integrated Systems, Vanderbilt Univ., Jan. 2010. Nashville.
[9] S. Bensalem, M. Bozga, T. Nguyen, J. Sifakis: D-Finder: A Tool for Compositional Deadlock Detection and Verification. CAV 2009: 614-619